## Slide 1
Group - 3
Lab Group 5-6
CT-216 PROJECT
Introduction to Communication Systems
Prof. Yash Vasavada
Mentor: Radhika Agrawal

## Slide 2
Polar Codes

## Slide 3
We as a group, declare that :
  The work that we are presenting is our own work.
  We have not copied the work (Python code, results, etc.)
that someone else has done.
  Wherever we have relied on an existing work that is not ours, we have provided a proper reference citation.
  The concepts, understanding, and insights we will be describing are our own.
  We make this pledge truthfully. We know that violation of this solemn pledge can carry grave consequences.
Honor code

## Slide 4
  Ayush Chaudhari -202201517
  Jemini Chaudhari- 202201521
  Arnold Mochahari- 202201522
  Yash Rathod - 202201524
  Elvis Kotadiya-202201526
  Natansh Shah - 202201445
  Devarsh Soni - 202201446
  Devarshi Patel - 202201447
  Vasoya Neel - 202201448
  Chirag Patel-202201512
Group Members

## Slide 5
Outline
  Introduction
  Block Diagram
  Polar Encoding
  Bit Channels and Polarization
  BPSK AND AWGN
  Brute Force Method (Hard Decoder)
  Successive Cancellation Decoder
  Successive Cancellation list Decoding

## Slide 6
1
Introduction
  Polar codes were introduced by Erdal Arıkan in 2008
  Polar codes are the first codes to reliably achieve channel capacity on binary memoryless symmetric channels through a straightforward deterministic construction process.
  When decoded using successive cancellation decoder it splits channel into sub bits channels and on increasing input bits sub bits converge
to purely noiseless channel or noisy channel.
Therefore they are channel-polarized.
  Encoded using Kronecker product
  Decoded in sequential order

## Slide 7
Block Diagram
Adding
CRC
Encode
BPSK +
AWGN
LIST
DECODE
msg
A
bits
K
bits
N
bits
K=A+L
(N,K) code
M : listsize
cword
CHECK
CRC
msg estimate
M
cwords
2

## Slide 8
Polar Encoding
Polar Transfrom G₂
G₂=
1
0
1
1
  [u1 u2]G = [u1+u2 u2]
u1
u2
X1
X2
y1
y2
BPSK
+
AWGN
x
Mapping from (u1,u2) to (X1,X2) is an invertible mapping
3

## Slide 9
Binary Tree Representation
u1
u2
[u1 u2]G = [u1+u2 u2]
1
0
1
1
G₂=
4

## Slide 10
Polar Transform General
G₂ⁿ=
x
n
NXN
Finding G matrix for general N
  N=
2
n
  u⁽ᴺ⁾= uG
N
  Binary Tree Representation
    depth=n
    u (message bits at the leaf nodes and u⁽ᴺ⁾ encoded messsage bits at the top
1
0
1
1
5

## Slide 11
G₄=
1
0
1
1
x
2
4X4
1
0
1
1
x
1
1
Polar Transform G₄
  N=4
  n=log₂(4)=2
  u⁽ᴺ⁾= uG = [u1+u2+u3+u4 u2+u4 u3+u4 u4]
N
0
1
1
0
1
1
1
0
1
1
1
0
1
1
0
0
0
0
1
1
6

## Slide 12
Binary Tree Representation G₄
u1
u2
u3
u4
[u1+u2 u2]
[u3+u4 u4]
[u1+u2+u3+u4 u2+u4 u3+u4 u4]
7

## Slide 13
N
G
BPSK
+
AWGN
X
rᴺ
uᴺ
Bit Channel 1
Bit Channel 2
Bit Channel 3
Bit Channel 4
u₁
u₂
u₃
rᴺ
rᴺ,u₁,u₂
rᴺ,u₁
u
N
rᴺ,u₁,u₂...u
N-1
Bit Channels and Polarization
As we increase the bit size the bit channels can be polarized either
very noisless or noisy and we can order them on their confidence level.
8
.
.
.
.
.

## Slide 14
Bit Channels and Polarization
9
How can we polarize a data channel into extremal good and bad channels?
Let W is a Binary Erasure Channel (BEC)
let X is fed into W
X is unsuccessfully decoded with probability p that is BEC is able to detect that bit has been erased.
X is successfully decoded into Y probability 1-p
  W⁻ : U₁ → (Y₁, Y₂)
  W⁺ : U₂ →(Y₁, Y₂)
W- tries to reconstruct input received on U1 channel
W+ tries to reconstruct input received on U2 channel.
  Image credit - https://medium.com/5g-nr/polar-codes-703336e9f26b

## Slide 15
Bit Channels and Polarization
10
How can we polarize a data channel into extremal good and bad channels?
U1 can only be decoded successfully decoded with probability (1-p)²
since U1 can be extracted from U1 xor U2 and U2 is successfully decoded.
And all other cases will unsuccessfull decode U1
U1 is successfully decoded with probability (1-p)²
U1 is unsuccessfully decoded with probability p(1-p) + (1-p)p + p² =2p-p²
let succcess probability 1-p=0.8 and unsuccess probability p=0.2
W- success probability = (1-p)² =0.64
W- unsuccess probability = p(1-p) + (1-p)p + p² =2p-p²=0.36
  Image credit - https://medium.com/5g-nr/polar-codes-703336e9f26b

## Slide 16
Bit Channels and Polarization
11
How can we polarize a data channel into extremal good and bad channels?
U2 can be successfully decoded in first and second case as U2 is received successfully .
In third case we have already decoded U1 and we have U1 xor U2 and therefore we can successfully decode U2 also.
In last case we can decode U2
U2 can be successfully decode with probability (1-p)² + p(1-p) + (1-p)p = 1-p²
U2 can be decoded unsuccessfully with probability p²
we have success probabilty from previous slide as 1-p = 0.8
and unsuccess probability p=0.2
W+ success probability = (1-p)² + p(1-p) + (1-p)p = 1-p² =0.96
W+ unsuccess probability = p²=0.04
As you can see that success probability is more in W+ than compared to W-.
  Image credit - https://medium.com/5g-nr/polar-codes-703336e9f26b

## Slide 17
Reliability Sequence
The reliability sequence in polar codes refers to a sequence of values assigned to each bit, indicating the confidence level in the correctness of that bit based on received channel information.
The reliability sequence is arranged in increasing order
eg : for N=8 [ 1 2 3 5 4 6 7 8]
12
Frozen Bits
Frozen bits in polar codes are specific bits that are known to both the encoder and the decoder and are set to predetermined values before transmission.
F=N−K
N= total number of bits
K = information bits

## Slide 18
u1
u2
u3
u4
u5
u6
m1
m2
m3
m4
0
0
0
0
(0 0)
(m1 m1)
(m2 m2)
u7
u8
(m3+m4 m4)
(m1 m1
m1 m1)
(m2+m3+m4 m2+m4
m3+m4 m4)
(N,K)=(8,4)
Polar Transform
(m1+m2+m3+m4 m1+m2+m4 m1+m3+m4 m1+m4 m2+m3+m4 m2+m4 m3+m4 m4)
13

## Slide 19
BPSK AND AWGN
Binary Phase Shift Keying (BPSK) :-
It is a modulation technique employed in communication systems to transmit information via a communication channel.
In BPSK the carrier signal is modified by altering its phase by 180 degrees, for each symbol. A phase shift of 180 degrees denotes a binary 0 while no phase shift represents a binary 1
s= 1-2b
if transmitted bit b =0 it is mapped to 1 , and if transmitted bit is 1 it is mapped to -1
14

## Slide 20
SNR = Ps/Pn=γ
Pn=Ps/SNR
where Ps = E{|x|²} is the mean power of the source and x is transmitted source
for bpsk .Ps=(-1²+1²)/2 =1
Noise added is
AWGN Additive White Gaussian Noise) :-
Uₛ~ N(0,1)
15

## Slide 21
Decoding
1) Brute Force Method
2) Successive Cancellation Decoding
3) Successive Cancellation List Decoding
  Various methods for decoding :
16

## Slide 22
Brute Force Method
Step 1) Demodulate the noisy codeword obtained after doing BPSK and
adding AWGN.
Make every bit of the noisy codeword that is positive (≥0) as 0, and all the negative bits (<0) as 1.
Example :-
Demodulated noisy codeword : [ 1 , 0, 0, 1 ]
17
Consider a noisy codeword for N=4, [ -1.524, 0.421, 0.685, -1.221 ]

## Slide 23
Step 2) Multiply the demodulated codeword with the inverse
of Gn, the output we get is our decoded codeword.
Consider demodulated codeword= d
decoded codeword = u
d
18
  We know, c=u*G , where u is the transmitted codeword, c is the encoded codeword (before BPSK and AWGN).
  Similarly d=u *G
  We can find u from this equation.
N
ᵈ
ᵈ
N

## Slide 24
Step 3) Compare u with u
ᵈ
  Thus if u= u , then we have correctly decoded the codeword.
  From this we can get our transmitted message by separating the frozen bits and message bits.
ᵈ
19
  Note: If c=d, then we are able to correctly reverse the effect of BPSK and AWGN and get back our encoded codeword.
  If not , we can find the number of errors by carrying out the xor operating between both of them and counting the number of 1's in the resulting sequence.

## Slide 25
  Advantages
  1. Easy to implement
  Disadvantages
20
  Unreliable
  It simply demodulates the noisy codeword without taking other factors into account , there is a chance that when noise generated has a magnitude greater than 1, it would lead to wrong bit being decoded.

## Slide 26
Successive Cancellation Decoder
In this decoding process, bits of the received signal are decoded sequentially, starting with eliminating the least reliable ones. Each bit's decoding relies on information from previously decoded bits and the received signal
G
N
u1
BPSK
+
AWGN
u4
u2
u3
r1
r2
r3
r4
x2
x3
x4
x1
rᴺ
xᴺ
xᴺ
uᴺ
is belief of
is belief of
21

## Slide 27
u1 = x1+x2
u2 = x2
x = [x1,x2] = [u1+u2,u2]
SC DECODER WITH N=2 subtree
belief (u1) = f(r1,r2) = sgn(r1).sgn(r2).min(|r1|,|r2|)
u1^ = 0 if belief(u1)>=0; u1^ = 1 if belief(u2)<0
g(r1,r2,b) =r2 + (1-2b)r1
Note - r1 refers to belief of x1 and r2 refers to belief of x2
22

## Slide 28
u1
u2
u3
u4
[f(L1,L2)]
[r1 r2 r3 r4]
[f(r1,r3) , f(r2,r4)]
[L1 , L2]
=
[g(L1,L2,u1^)]
[f(L3,L4)]
[r3,r4]
[L3,L4]
=
[g(L3,L4,u3^)]
[u1^+u2^+u3^+u4^, u2^+u4^,
u3^+u4^ , u4^]
f(L1,L2) = sgn(L1).sgn(L2).min(|L1|,|L2|)
g(L1,L2,b) =L2 + (1-2b)L1
SC DECODER WITH N=4 subtree
23

## Slide 29
24
  Image credit - Tahir, B. (2017). Construction and performance of polar codes for transmission over the AWGN channel [Diploma Thesis, Technische Universität Wien]. reposiTUm. https://doi.org/10.34726/hss.2017.50228

## Slide 30
25
  The above graph shows that at a very low value of Eb/N0 i.e. for the high value of Spectral Density of noise, the probability of successful decoding tends to zero, but as the value of Eb/N0 increases, the rate of increasing probability of successful decoding becomes exponentially high.
  Also after a certain value of Eb/N0 , the probability of successful decoding becomes nearly equal to 1.

## Slide 31
26
Observing for various values for (N,K)
  The above graph shows bit error rate for various values of r = K/N. More is the ration of the redundant bits in the codeword transmitted , lesser are the possibilities of getting error in transmission for particular value of SNR.

## Slide 32
27
  Same thing can be observed from taking the BER value in log scale also , same observation can be made on how drastically error reduces for a particular increase in Eb/N0.

## Slide 33
Positives of SC-Decoder
  Has comparatively lower time complexity for decoding, also due to sequential execution, it becomes easy to execute in real hardware systems.
  As the block length increases up to an extent, then channels become very polarized, making channels either very good or very bad which leads to filtering and thus faster execution and high probability of successful decoding.
  Predictable latency due to sequential execution as current progress can be seen to predict the total time for execution.
Drawbacks for SC-Decoder
28
  A significant issue for the SC-decoder is that it decodes the current value as being dependent on the past bit value, any error in even a single bit can lead to a change in a message at the receiver end, so on compounding multiple errors this can lead to a drastic change in message bits.
  Another major drawback is that the Sequential Decoding Algorithm is sequential in nature which leads to slower execution, so increasing the latency of the algorithm and very high execution time.

## Slide 34
NOTE - A SIGNIFICANT INCREASE IN PERFORMANCE IS NOTICED IN THE ABOVE GRAPH
29
Direct Demodulation vs Successive Decoding Technique
For N = 512 , K = 256

## Slide 35
Successive Cancellation List Decoding
30
Adding
CRC
Encode
BPSK +
AWGN
LIST
DECODE
CHECK
CRC
msg
A
bits
K
bits
N
bits
K=A+L
(N,K) code
M : listsize
msg estimate
cword
M
cwords
  SC Decoding - any decoding error can propagate and later adversely affect the decoding of furthermore subsequent bits
  List Decoding - Proposes a list of the most favorable codewords instead of one codeword, the number of codewords depending upon the requirement of the system.
  To choose from the given list, there is padding of CRC bits used, namely called Cyclic Redundancy Test.
  CRC is used only for Error-detection in codes, it though cannot be exploited to much help in error-correction.
  Works similar to what Parity did in Single Parity Check (SPC) codes.

## Slide 36
What is Cyclic Redundancy Check (CRC)??
31
  CRC is a method used for error detection for Polar Codes data sequence transmitted over a channel.
  This is done by adding some fixed length CRC bits padding at the end of message bits, thus information bits contain both message bits and CRC bits.
  CRC check is done at both transmitter and receiver end such that the message bits’ binary values when using a coefficient for a polynomial then polynomial formed by CRC bits as coefficient divides it for remainder zero.
  If the remainder obtained at the receiver side does not yield zero, then it means that error has a role to play in the received message.

## Slide 37
How does CRC WORK ??
  Let the data be 1001101 and the binary equivalent of the generic polynomial is 1011. On the sender side, the remainder can be found using binary division as follows.
  The remainder of the above division is 101. This remainder is appended to the data to create the signal which will be sent to the receiver. The signal is 1001101101.
Example Credit-
https://www.scaler.com/topics/crc-program-in-c/
32

## Slide 38
Example Credit-https://www.scaler.com/topics/crc-program-in-c/
  As the remainder is 111, we can assure that there is an error in the message.
33

## Slide 39
Path Metrics , Decision Metrics
  In context of Succession List Decoding , parameters like Path Metrics , Decision Metrics have an important role to play to decide which out of all generated codewords is most efficient and close to the message transmitted and contains least of all errors.
  Decision Matric basically means belief of the node.
  Path metric represents the sum of all the decision metrics along in that path
34
How to produce multiple codewords ?
  Consider both decisions for each bit and assign the decision metric (DM) for it.
  If L(UI)>=0, ui^ = 0 has decision metric DM = 0; and ui^=1 will have decision metric DM = | L(ui) |;
  If L(UI)<0, ui^ = 1 has decision metric DM = 0; and ui^=0 will have decision metric DM = | L(ui) |;
  For frozen bits also, when we take a decision against the belief then we need to have DM = | | L(ui) |;
  Path metric is the sum of decision metrics.
Path Metric thus represents total penalty cost for corresponding particular codeword , lower the Path metric , better is the probability of codeword being correct.

## Slide 40
  Main abstract of this method is that we perform Successive decoding paralelly for nL decoders and calculate path metrics for each generated codeword and when number of codewords exceen nL , then we prune the branches for codewords with highest path metrics and end up getting nL codewords with lowest path metric and highest probability of success amongst others.
  All of the nL codewords might not be correct but at the end of traversal , we check for Cyclic Redundancy Check in all nL codewords and consider the one which has passed CRC check and has lowest path metric.
  In some cases it might occur that none of them actually passes CRC check then , we filter them on bases of path metric only and consider the one with lowest path metric as final decoder codeword.
How Successive List Decoding Works ?
35
Figure represented on next page actually explains for temporary list sized growth for branches showing generation and reduction for actual nL codewords up to a extent.

## Slide 41
Temporary List size growth in Successive List Decoding with nL = 4
36
Image credits - Kim, Jong-Hwan & Kim, Sang-Hyo & Jang, Ji-Woong & Kim, Young-Sik. (2017). Low Complexity List Decoding for Polar Codes with Multiple CRC Codes. Entropy. 19. 183. 10.3390/e19040183.

## Slide 42
Performance of a Successive List Decoder for various valuesof N and k
37
  All the positives for the Successive Cancellation Decoder also hold for the List Decoder. Still, over larger values, we can observe the difference in the performance of the list decoder vs sc decoder.
  Another observation holds that as the value of N increases in ratio to K, the probability of success increases.

## Slide 43
38

## Slide 44
Performace of List Decoder under r = 0.5
39
For N = 64 , K = 39

## Slide 45
40
Performance Improvement in moving to List Decoder vs SC-Decoder
  As we can observe from the above plot , we can have a significant change in performance at even low values of SNR over a number of simulations and this can be considered as a significant improvement in channel decoding perspective for error-correcting codes
For N = 64 , K = 39

## Slide 46
41
Performance Improvement in moving to List Decoder vs SC-Decoder
  The above plot shows a bit error rate comparison for SC-Decoder and List Decoder for multiple simulations, as we can observe the bit error rate is quite lower in List Decoder than in SC-Decoder which should also be the case.
For N = 64 , K = 39

## Slide 47
42
Performance Improvement in List Decoder when increased value of number of generated codewords
For N = 64 , K = 39

## Slide 48
For N = 64 , K = 39
For N = 64 , K = 39

## Slide 49
  Image credit - Tahir, B. (2017). Construction and performance of polar codes for transmission over the AWGN channel [Diploma Thesis, Technische Universität Wien]. reposiTUm. https://doi.org/10.34726/hss.2017.50228
43
  The above images show the difference it would make for the efficiency of the received bit when we increase nL i.e. the maximum number of codewords that can be simultaneously generated.
  As we increase the number of decoders we increase in recognizing the margin of error and try to eliminate most of them by having a greedy approach when we need to select branches to prune for generating codewords.

## Slide 50
Theoretical BER with BER for SC-Decoder and List Decoder
44

## Slide 51
  Image credit - Tahir, B. (2017). Construction and performance of polar codes for transmission over the AWGN channel [Diploma Thesis, Technische Universität Wien]. reposiTUm. https://doi.org/10.34726/hss.2017.50228
45
  The above shows the difference and gradual increase in efficiency as we move ahead in the methods we used for decoding the polar encoding done at the channel side.
  As we can observe the difference it makes when we use the List-Sc decoder in place of the SC-Decoder and when we use the CRC bits for error detection we can definitely observe an upgrade when simulated over a long keyword for a high number of simulations.

## Slide 52
Thank you